## Slide 1
Protocol Layering - Introduction
Protocol
  Rules that both the sender and receiver and all intermediate devices need to follow to be able to communicate effectively
Protocol Layering
  Simple Communication: only one simple protocol
  Complex Communication, we need a protocol at each layer, or Protocol Layering

## Slide 2
Protocol Layering - Example Scenario 1

## Slide 3
Protocol Layering - Example Scenario 2

## Slide 4
Protocol Layering - Advantages and Disadvantages
Advantages
  Modularity
  Separation of Service & Implementation
  Reduced Complexity &
  Cost
Disadvantages
  None Really!

## Slide 5
Protocol Layering - Principles
Two Principles
  Bidirectional Communication  Each Layer performs two opposite tasks in each direction
  Two objects under each layer at both sites should be identical

## Slide 6
Protocol Layering - Logical Connections
Logical Connections
  Imaginary connection between each layer

## Slide 7
Protocol Layering

## Slide 8
TCP/IP Protocol Suite
TCP/IP Protocol Suite
  Protocol suite used in Internet today
  Each Layer provides specific functionality
  Hierarchical Protocol
  Presented in 1973 and chosen to be the official protocol of Internet in 1983

## Slide 9
TCP/IP Protocol Suite

## Slide 10
TCP/IP Protocol Suite - Layered Architecture

## Slide 11
TCP/IP Protocol Suite – Function of Layers
Logical Connections between TCP/IP Layers

## Slide 12
TCP/IP Protocol Suite – Function of Layers
Logical connections

## Slide 13
Identical objects (messages)
Identical objects (segment or user datagram)
Identical objects (datagram)
Identical objects (frame)
Identical objects (bits)
Identical objects (datagram)
Identical objects (frame)
Identical objects (bits)
TCP/IP Protocol Suite – Function of Layers

## Slide 14
TCP/IP Protocol Suite – Layer Description

## Slide 17
Encapsulation & Decapsulation
Important Concept in Internet Protocol Layering
Layer Header

## Slide 18
Encapsulation & Decapsulation

## Slide 19
Addressing in TCP/IP Protocol Suite
Every communication needs at least two addresses:
  Source Address &
  Destination Address
Addressing by Layer
Physical Layer is an exception

## Slide 20
Addressing in TCP/IP Protocol Suite

## Slide 21
The Open System Interconnection (OSI) Model
International Organization for Standardization (ISO)
ISO established in 1947
Close to three-fourths of countries represented
Introduced OSI Model in late 1970s
OSI: a 7-Layer Model

## Slide 22
The Open System Interconnection (OSI) Model

## Slide 23
OSI Model vs TCP/IP Protocol suite
Two Layers of OSI missing from TCP/IP
Application (TCP/IP) = Application + Presentation + Session (OSI)

## Slide 24
OSI Model vs TCP/IP Protocol suite

## Slide 25
Lack of OSI Model’s Success
Three reasons OSI did not replace TCP/IP:
  OSI was completed when TCP/IP was fully in place
  Some layers in OSI not fully defined
  Performance of TCP/IP better than that of OSI

## Slide 26
Data Communication versus Computer Networks

## Slide 27
Data Communication versus Computer Networks
Analog & Digital Transmission
Transmission Media
Switching
Error Detection and Correction
Media Access and Data Link Control
Wired and Wireless LANs