## Slide 1
Switching
A network is a set of connected devices
Problem of how to connect multiple devices to make one-to-one communication possible
The solution is Switching
Switched network consists of a series of switches

## Slide 2
Switched Network

## Slide 3
Three Methods of Switching
Three Methods:
  Circuit Switching
  Packet Switching
  Message switching
The first two are commonly used today
The third has been phased out in general communications

## Slide 4
Taxonomy of Switched Networks

## Slide 5
Circuit-switched Networks
A set of switches connected by physical links
A connection between two stations is a dedicated path made of one or more links
Each connection uses only one dedicated channel on each link
Each link is normally divided into n channels by using FDM or TDM

## Slide 6
Circuit-switched Networks
A set of switches connected by physical links

## Slide 7
A Circuit-Switched Network

## Slide 8
As a trivial example, let us use a circuit-switched network to connect eight telephones in a small area. Communication is through 4-kHz voice channels. We assume that each link uses FDM to connect a maximum of two voice channels. The bandwidth of each link is then 8 kHz.
Example

## Slide 9
As another example, consider a circuit-switched network that connects computers in two remote offices of a private company. The offices are connected using a T-1 line leased from a communication service provider. There are two 4 × 8 (4 inputs and 8 outputs) switches in this network.
Example

## Slide 10
Three Phases in a Circuit Switched Network
The actual communication in a circuit-switched network requires 3 phases:
  Connection Setup
  Data Transfer
  Connection Teardown

## Slide 11
Three Phases in a Circuit Switched Network

## Slide 12
Efficiency of a Circuit-Switched Network
Not as efficient as packet switching because resources are allocated during the entire duration of the connection and these resources are unavailable to other connections

## Slide 13
Efficiency of a Circuit-Switched Network
In a telephone network, people normally terminate the communication when they have finished their conversation
Data Network is an issue

## Slide 14
Delay in a Circuit-Switched Network
Circuit switched networks have low efficiency but minimal delay
Data is not delayed at each switch; the resources are allocated for the duration of the connection

## Slide 15
Delay in a Circuit-Switched Network

## Slide 16
Packet Switching
If the message is going to pass through a packet-switched network, it needs to be divided into packets of fixed or variable size
The size of the packet is determined by the network and the governing protocol

## Slide 17
Datagram Networks
Each packet is treated independently of all others.
Even if a packet is part of a multi-packet transmission, the network treats it as though it existed alone
Packets are referred to as datagrams

## Slide 18
Virtual-Circuit Networks
A virtual-circuit network is a cross between a circuit-switched network and a datagram network

## Slide 19
Virtual-circuit network

## Slide 20
Virtual-Circuit Networks
A virtual-circuit network is a cross between a circuit-switched network and a datagram network

## Slide 21
Virtual-Circuit Networks

## Slide 22
Virtual-Circuit Networks
A virtual-circuit network is a cross between a circuit-switched network and a datagram network

## Slide 23
Virtual-Circuit Identifier

## Slide 24
Switch & table for a virtual-circuit network

## Slide 25
Structure Of A Circuit Switch
Circuit switching today can use either of two technologies:
  The Space-Division switch
  The Time-Division switch

## Slide 26
Crossbar switch with 3 inputs & 4 outputs

## Slide 27
Multistage Switch

## Slide 28
Time-Division Switch
Uses TDM inside a switch
Most popular technology is Time-Slot Interchange (TSI)

## Slide 29
Time-Division Switch