## Slide 1
Data-Link Layer
The Internet is a combination of networks glued together by connecting devices (routers or switches)
If a packet is to travel from a host to another host, it needs to pass through these networks
Data Link layer controls node-to-node communication

## Slide 2
Communication at the Data-Link Layer

## Slide 3
Nodes and Links
Communication at the data-link layer is node-to-node
A data unit from one point in the Internet needs to pass through many networks (LANs and WANs) to reach another point
We refer to the two end hosts and the routers as nodes and the networks in between as links

## Slide 4
Nodes and Links

## Slide 5
Services provided by Data-Link Layer
Located between the physical and the network layers
Provides services to Network Layer and receives services from Physical layer
Framing
Flow Control
Error Control
Congestion Control

## Slide 6
A Communication with only Three Nodes

## Slide 7
Two nodes are physically connected by a transmission medium such as cable or air
Data-link layer controls how the medium is used
  Data-link layer can use whole capacity
  Data-link layer can use only part of the capacity
Two Categories of Links

## Slide 8
We can have the following two types of links:
  Point-to-point link or a
  Broadcast link
Two Categories of Links

## Slide 9
We can divide the data-link layer into two sublayers:
  Data Link Control (DLC)
  Media Access Control (MAC)
Two Sublayers of Data-Link Layer

## Slide 10
Dividing the data-link layer into two sublayers

## Slide 11
IP addresses are the identifiers at the network layer
In Internet we cannot make a packet reach its destination using only IP addresses
Source and destination IP addresses define the two ends but cannot define which links the packet will take
Why LINK-LAYER ADDRESSING?

## Slide 12
IP addresses & Link-Layer Addresses

## Slide 13
Three Types of addresses
Some link-layer protocols define three types of addresses:
Unicast
Multicast
Broadcast

## Slide 14
Example
The unicast link-layer addresses in the most common LAN, Ethernet, are 48 bits (six bytes) that are presented as 12 hexadecimal digits separated by colons; for example, the following is a link-layer address of a computer. The second digit needs to be an odd number.
A3:34:45:11:92:F1

## Slide 15
Example
The multicast link-layer addresses in the most common LAN, Ethernet, are 48 bits (six bytes) that are presented as 12 hexadecimal digits separated by colons. The second digit, however, needs to be an even number in hexadecimal. The following shows a
multicast address:
A2:34:45:11:92:F1

## Slide 16
Example
The broadcast link-layer addresses in the most common LAN, Ethernet, are 48 bits, all 1s, that are presented as 12 hexadecimal digits separated by colons. The following shows a broadcast address:
FF:FF:FF:FF:FF:FF

## Slide 17
Address Resolution Protocol (ARP)
Anytime a node has an IP packet to send to another node in a link, it has the IP address of the receiving node
IP address of the next node is not helpful in moving a frame through a link; we need the link-layer address of the next node

## Slide 18
Address Resolution Protocol (ARP)
We need Address Resolution Protocol (ARP)

## Slide 19
Position of ARP in TCP/IP protocol suite

## Slide 20
ARP Operation

## Slide 21
ARP Packet

## Slide 22
The internet for our example

## Slide 23
Flow of packets at Alice site

## Slide 24
Flow of activities at router R1

## Slide 25
Flow of activities at router R2

## Slide 26
Activities at Bob’s site