## Slide 1
Data Link Control (DLC) Services
The data link control (DLC) deals with procedures for communication between two adjacent nodes no matter whether the link is dedicated or broadcast
Data link control functions include framing, flow control and error control

## Slide 2
DLC Services
DLC Services
Framing
Error Control
Flow Control

## Slide 3
Framing
Data-Link layer needs to pack bits into frames, so that each frame is distinguishable from another
Our postal system practices a type of framing
Framing separates a message by adding a sender address and a destination address

## Slide 4
Framing
The destination address defines where the packet is to go; the sender address helps the recipient acknowledge the receipt

## Slide 5
Frame Size
Why not one BIG Frame?
Frames can be of:
  Fixed Size
    Size acts as a boundary/delimiter
  Variable Size
    How to define Beginning and End of a Frame?

## Slide 6
Variable Framing Techniques
Variable Framing Techniques
Character Oriented Framing
Bit Oriented Framing

## Slide 7
A Frame in a Character-Oriented Protocol

## Slide 8
Connection Oriented Framing
Data to be carried are 8-bit characters

## Slide 9
Byte Stuffing in Connection-Oriented Framing
Connection-oriented Framing used text characters as flags
Nowadays any character used for flag can also be a part of the data
In order to avoid confusing the receiver, we use Byte Stuffing

## Slide 10
Byte Stuffing in Connection-Oriented Framing
Several Issues:
  One or more escape characters followed by a byte with same pattern as a flag?
  Unicode (16/32 bit) vs. 8-bit characters
Data is stuffed with a pre-defined Escape Character (byte) when there is a character with same pattern as a flag

## Slide 11
Byte Stuffing and Unstuffing

## Slide 12
Bit-Oriented Framing
Data section of frame is a sequence of bits
We need a delimiter to separate one frame from the other
A special 8-bit pattern (01111110) to define beginning and end of a frame
Same issue as Connection-oriented Framing

## Slide 13
A Frame in a Bit-Oriented Protocol

## Slide 14
Bit Stuffing and Unstuffing

## Slide 15
Flow and Error Control
One of the responsibilities of the data-link control sublayer is flow and error control at the data-link layer

## Slide 16
Flow Control
Balance between production and consumption rates
If frames are produced faster than they are consumed at the receiving data link layer, the frames will be discarded
Use of buffers; one at sending end and other at receiving end

## Slide 17
Flow Control at the Data Link Layer

## Slide 18
Example
Consumers need to communicate with the producers on two occasions:
  When the buffer is full; &
  When there are vacancies
If the two parties use a buffer with only one slot, the communication can be easier

## Slide 19
Error Control
Error Control at Data Link layer uses CRC in one of the two ways:
  If a frame is corrupted, it is silently discarded and if it is good, it is delivered to network layer
  If frame is corrupted, it is silently discarded and if it is good, an acknowledgement is sent to sender

## Slide 20
A DLC protocol can be either connectionless or connection-oriented
Connectionless: No relationship between the frames
Connection-Oriented: Frames are numbered and sent in order
Connectionless and Connection-Oriented

## Slide 21
A machine with a finite number of states
Machines stays in one of the states until an event occurs
Each event is associated with 2 reactions:
  List of actions to be performed
  Determining the next state
Finite State Machine (FSM)

## Slide 22
Finite State Machine (FSM)

## Slide 23
Traditionally four protocols have been defined for the data-link layer to deal with flow and error control:
  Simple Protocol
  Stop-and-Wait Protocol
  Go-Back-N Protocol
  Selective-Repeat Protocol
DATA-LINK LAYER PROTOCOLS

## Slide 24
Simple protocol has neither flow nor error control
Assumption: The receiver can immediately handle any frame it receives
The receiver can never be overwhelmed with incoming frames
Simple Protocol

## Slide 25
Simple Protocol

## Slide 26
FSM for Simple Protocol

## Slide 27
Here is an example of communication using this protocol. It is very simple. The sender sends frames one after another without even thinking about the receiver.
Example

## Slide 28
Stop-and-Wait protocol uses both flow and error control
The sender sends one frame at a time and waits for an acknowledgment before sending the next one
To detect corrupted frames, we add a CRC code
Stop-and-Wait Protocol

## Slide 29
Stop-and-Wait Protocol

## Slide 30
Example

## Slide 31
Example

## Slide 32
Both Simple and Stop-and-wait protocols are designed for unidirectional communication
Data flows in one direction and ACK travels in the other
To make the system efficient, the data in one direction is piggybacked with the acknowledgment in the other direction
Piggybacking

## Slide 33
Bit -oriented protocol for communication over point-to-point and multipoint links
It implements Stop-and-Wait protocol
Most of the concepts defined in this protocol is the basis for other protocols such as PPP, Ethernet, or wireless LANs
High-level Data Link Control (HDLC)

## Slide 34
HDLC provides two common transfer modes that can be used in different configurations:
  Normal Response Mode (NRM) &
  Asynchronous Balanced Mode (ABM)
Configurations & Transfer Modes in HDLC

## Slide 35
Normal Response Mode

## Slide 36
Asynchronous Balanced Mode

## Slide 37
HDLC defines three types of frames:
  information frames (I-frames)
  Supervisory frames (S-frames)
  Unnumbered frames (U-frames)
Framing

## Slide 38
HDLC Frames

## Slide 39
Most common protocol for point-to-point access
Millions of Internet users who need to connect their home computers to the server of an Internet service provider use PPP
To control and manage the transfer of data, there is a need for a PPP at the data-link layer
Point-to-Point Protocol (PPP)

## Slide 40
The designers of PPP have included several services to make it suitable for a point-to-point protocol, but have ignored some traditional services to make it simple
Services provided by PPP
Services Included | Services Not Included
Framing | Flow Control
Link Establishment and Data Exchange | Error Correction (PPP has CRC detection only)
Authentication | No Sequence Numbering
Multilink PPP Address configuration | Absence of sophisticated Addressing Mechanism
Network Address configuration | 

## Slide 41
PPP Frame Format
PPP uses a character-oriented (or byte-oriented) frame

## Slide 42
Although PPP is a link-layer protocol, it uses another set of protocols to establish the link, authenticate and carry the network-layer data
Three sets of protocols are:
  Link Control Protocol (LCP)
  Two Authentication Protocols (APs)
  Several Network Control Protocols (NCPs)
Multiplexing in PPP

## Slide 43
Multiplexing in PPP

## Slide 44
LCP Packet encapsulated in a Frame

## Slide 45
LCP Packets

## Slide 46
Authentication Protocols in PPP
PPP Authentication
Password Authentication Protocol
(PAP)
Challenge Handshake Authentication Protocol
(CHAP)

## Slide 47
PAP packets encapsulated in a PPP frame

## Slide 48
CHAP Packets encapsulated in a PPP frame

## Slide 49
Internet Protocol Control Protocol (IPCP)

## Slide 50
Code values for IPCP Packets

## Slide 51
IP datagram encapsulated in a PPP frame