## Slide 1
When nodes use a multipoint or broadcast link, we need a multiple-access protocol to coordinate access to the link
Many protocols have been devised to handle access to a shared link
All of these protocols belong to Media Access Control (MAC) sub-layer
Media Access Control (MAC) Sub-Layer

## Slide 2
Taxonomy of Multiple-Access Protocols

## Slide 3
Random Access
In random-access or contention no station is superior to the other and none is assigned control over the other
Station that has data to send uses a procedure defined by the protocol to make a decision on whether or not to send
This decision depends on the state of the medium (idle or busy)

## Slide 4
ALOHA
ALOHA, the earliest random access method, was developed in early 1970s
Designed for a radio (wireless) LAN, but it can be used on any shared medium
Potential collisions in this arrangement as the medium is shared between the stations

## Slide 5
ALOHA
When a station sends data, another station may attempt to do so at the same time
The data from the two stations collide and become garbled

## Slide 6
Frames in a pure ALOHA network

## Slide 7
Procedure for pure ALOHA protocol

## Slide 8
Vulnerable Time for pure ALOHA protocol

## Slide 9
Slotted ALOHA
We divide time into slots of Tfr sec and force the station to send only at the beginning of the slot
Invented to improve the efficiency of pure ALOHA
If a station misses the time slot, it must wait until beginning of next time slot reducing vulnerable time to Tfr (vs. 2 x Tfr for pure ALOHA)

## Slide 10
Frames in a Slotted ALOHA Network

## Slide 11
Vulnerable Time for Slotted ALOHA

## Slide 12
To minimize the chance of collision and, therefore, increase the performance, CSMA was developed
The chance of collision is reduced as the station is required to sense/listen to the medium before sending data
‘sense before transmit’ or ‘listen before talk’
Carrier Sense Multiple Access (CSMA)

## Slide 13
Space/Time Model of a Collision in CSMA

## Slide 14
Vulnerable Time in CSMA

## Slide 15
Behavior of Three Persistence Methods

## Slide 16
CSMA method does not specify the procedure following a collision
CSMA/CD augments the algorithm to handle the collision
The station monitors the medium after it sends a frame to see if the transmission was successful. If there is a collision, the frame is sent again
Carrier Sense Multiple Access/Collision Detection

## Slide 17
Collision of the First Bits in CSMA/CD

## Slide 18
Collision and Abortion in CSMA/CD

## Slide 19
Flow Diagram for the CSMA/CD

## Slide 20
Energy Level During Transmission, Idleness and Collision

## Slide 21
CSMA/CA was invented for Wireless Networks
Collisions are avoided through the use of three strategies:
  The Interfame Space
  The Contention Window
  Acknowledgements
Carrier Sense Multiple Access/Collision Avoidance

## Slide 22
Flow Diagram for CSMA/CA

## Slide 23
Interframe Space (IFS): Collisions are avoided by deferring transmission even if the channel is idle
Contention Window: Amount of time divided into slots. Station chooses a random number of slots as its wait time (one slot first time and double each time system cannot detect an idle channel)
CSMA/CA

## Slide 24
Contention Window

## Slide 25
Acknowledgement: Positive acknowledgement and time-out timer can help guarantee that the receiver has received the frame
CSMA/CA

## Slide 26
CSMA/CA and Network Allocation Vector (NAV)

## Slide 27
The stations consult one another to find which station has the right to send
A station cannot send unless authorized by other stations
We discuss three controlled-access methods:
  Reservation
  Polling
  Token Passing
CONTROLLED ACCESS

## Slide 28
In the reservation method, a station needs to make a reservation before sending data
Time is divided into intervals
In each interval, a reservation frame precedes the data frames sent in that interval
Reservation

## Slide 29
Reservation Access Method

## Slide 30
Polling works with topologies in which one device is designated as a primary station and the other devices are secondary stations
All data exchanges must be made through primary device even when the ultimate destination is a secondary device
Polling

## Slide 31
The primary device controls the link; the secondary devices follow its instructions
Polling

## Slide 32
Select and Poll Functions in Polling-Access Method

## Slide 33
In the token-passing method, the stations in a network are organized in a logical ring
For each station, there is a predecessor and a successor
The predecessor is the station which is logically before the station in the ring; the successor is the station which is after the station in the ring
Token Passing

## Slide 34
Special packet called TOKEN circulates through the ring
Possession of TOKEN gives the station the right to send the data
TOKEN Management is required to manage possession time, Token monitoring, priority assignment etc.
Token Passing

## Slide 35
Logical Ring & Physical Topology in Token-Passing Method

## Slide 36
The available bandwidth of a link is shared in time, frequency, or through code, among different stations
We discuss three protocols:
  Frequency Division Multiple Access (FDMA)
  Time Division multiple Access (TDMA)
  Code Division Multiple Access (CDMA)
CHANNELIZATION (Channel Partition)

## Slide 37
In FDMA, the available bandwidth is divided into frequency bands
Each station is allocated a band to send its data i.e. each band is reserved for a specific station, and it belongs to the station all the time
Each station also uses a bandpass filter to confine the transmitter frequencies
Frequency-Division Multiple Access (FDMA)

## Slide 38
Frequency-Division Multiple Access (FDMA)

## Slide 39
Stations share the bandwidth of the channel in time
Each station is allocated a time slot during which it can send data
Each station transmits its data in its assigned time slot
TDMA

## Slide 40
Time-Division Multiple Access (TDMA)

## Slide 41
CDMA differs from FDMA in that only one channel occupies the entire bandwidth of the link
CDMA differs from TDMA in that all stations can send data simultaneously; there is no timesharing
Code Division Multiple Access (CDMA)

## Slide 42
Simple idea of Communication with Code

## Slide 43
Data Representation in CDMA