## Slide 1
Ethernet Protocol
Data-link layer and the physical layer are the territory of the local and wide area networks
We can have wired or wireless networks

## Slide 2
IEEE Project 802
In 1985, the Computer Society of the IEEE started a project, called Project 802, to set standards to enable inter-communication among equipment from a variety of manufacturers
Project 802 did not seek to replace any part of the OSI model or TCP/IP protocol suite

## Slide 3
IEEE Project 802
A way of specifying functions of the physical layer and the data-link layer of major LAN protocols

## Slide 4
IEEE Standard for LANs

## Slide 5
The Ethernet LAN was developed in the 1970s
Since then, it has gone through four generations:
  Standard Ethernet (10 Mbps)
  Fast Ethernet (100 Mbps)
  Gigabit Ethernet (1 Gbps)
  10 Gigabit Ethernet (10 Gbps)
Ethernet Evolution

## Slide 6
Ethernet Evolution

## Slide 7
The original Ethernet technology with the data rate of 10 Mbps is called Standard Ethernet
Most implementations have moved to later evolutions
Still some features of the Standard Ethernet that have not changed during the evolution
Standard Ethernet

## Slide 8
Each frame is independent of other
No connection establishment or tear down process
The sender may overwhelm receiver with frames and frames are dropped
If frame drops, sender will not know about it unless we are using TCP (Transport)
Connectionless & Unreliable Service

## Slide 9
Ethernet is unreliable like IP and UDP
If a frame is corrupted, receiver silently drops it
Left to high level protocols to find out abut it
Connectionless & Unreliable Service

## Slide 10
Ethernet Frame Format

## Slide 11
Each station on Ethernet has its own network interface card (NIC)
The NIC fits inside the station and provides the station with a link-layer/physical address
The Ethernet address is 6 bytes (48 bits), normally written in hexadecimal notation, with a colon between the bytes
Addressing in Standard Ethernet

## Slide 12
For example, the following shows an Ethernet MAC address:
4A:30:10:21:10:1A
Addressing

## Slide 13
How the address 47:20:1B:2E:08:EE is sent out online.
The address is sent left to right, byte by byte; for each byte, it is sent right to left, bit by bit, as shown below:
Transmission of Address Bits

## Slide 14
Unicast and Multicast Addresses

## Slide 15
Define the type of the following destination addresses:
4A:30:10:21:10:1A
47:20:1B:2E:08:EE
FF:FF:FF:FF:FF:FF
Example 13.2
To find the type of the address, we need to look at the second hexadecimal digit from the left. If it is even, the address is unicast. If it is odd, the address is multicast. If all digits are Fs, the address is broadcast. Therefore, we have the following:
This is a unicast address because A in binary is 1010 (even).
This is a multicast address because 7 in binary is 0111 (odd).
This is a broadcast address because all digits are Fs in hexadecimal.

## Slide 16
Implementation of Standard Ethernet

## Slide 17
Since the network that uses the standard Ethernet protocol is a broadcast network, we need to use an access method to control access to the sharing medium
The standard Ethernet chose CSMA/CD with 1-Persistent Method
Access Method in Standard Ethernet

## Slide 18
Access Method in Standard Ethernet

## Slide 19
The ratio of the time used by a station to send data to the time the medium is occupied by this station
The practical efficiency of standard Ethernet has been measured to be:
Efficiency = 1/(1+ 6.4 x a)
  where a = number of frames that can fit on a medium
Efficiency of Standard Ethernet

## Slide 20
In the Standard Ethernet with the transmission rate of 10 Mbps, we assume that the length of the medium is 2500 m and the size of the frame is 512 bits. The propagation speed of a signal in a cable is normally 2 × 108 m/s.
Example

## Slide 21
The Standard Ethernet defined several implementations, but only four of them became popular during the 1980s
Implementation of Standard Ethernet

## Slide 22
Summary of Standard Ethernet implementations

## Slide 23
Encoding in Standard Ethernet

## Slide 24
10Base5 implementation

## Slide 25
10Base2 implementation

## Slide 26
10Base-T implementation

## Slide 27
10Base-F implementation

## Slide 28
The changes that occurred to the 10-Mbps Standard Ethernet opened the road to the evolution of the Ethernet to become compatible with other high-data-rate LANs
  Bridged Ethernet
  Switched Ethernet
  Full-Duplex Ethernet
Changes in the Standard

## Slide 29
Bridged Ethernet- Sharing Bandwidth

## Slide 30
A Network with and without Bridging

## Slide 31
Switched Ethernet

## Slide 32
Full – Duplex Switched Ethernet

## Slide 33
In the 1990s, Ethernet made a big jump by increasing the transmission rate to 100 Mbps, and the new generation was called the Fast Ethernet
To make it compatible with the Standard Ethernet, the MAC sublayer was left unchanged
Fast Ethernet

## Slide 34
But the features of the Standard Ethernet that depend on the transmission rate, had to be changed
Goals of Fast Ethernet:
  Upgrade data rate to 100Mbps
  Make it compatible with Standard Ethernet
  Keep same 48-bit address
  Keep same frame format
Fast Ethernet

## Slide 35
To be able to handle a 100 Mbps data rate, several changes need to be made at the physical layer
Physical Layer

## Slide 36
Encoding for Fast Ethernet

## Slide 37
Implementation of Fast Ethernet implementations

## Slide 38
Need for an even higher data rate resulted in the design of IEEE Standard 802.3z Gigabit Ethernet Protocol (1000 Mbps)
Gigabit Ethernet

## Slide 39
The goals of the Gigabit Ethernet were:
  Upgrade the data rate to 1 Gbps
  Make it compatible with standard or Fast Ethernet
  Use same 48 bit address
  Use the same frame format
  Keep same minimum and maximum frame lengths
Gigabit Ethernet

## Slide 40
A main consideration in the evolution of Ethernet was to keep the MAC sublayer untouched
To achieve a data rate of 1 Gbps, this was no longer possible
Gigabit Ethernet has two distinctive approaches for medium access:
  Half-duplex
  Full-duplex
MAC Sub-layer

## Slide 41
The physical layer in Gigabit Ethernet is more complicated than that in Standard or Fast Ethernet
We briefly discuss some features of this layer:
Physical Layer

## Slide 42
Encoding in Gigabit Ethernet

## Slide 43
Summary of Gigabit Ethernet Implementations

## Slide 44
The idea is to extend the technology, the data rate, and the coverage distance so that the Ethernet can be used in LANs and MANs (metropolitan area network)
The IEEE committee created 10 Gigabit Ethernet and called it Standard 802.3ae
10-gigabit Ehternet

## Slide 45
10 Gigabit Ethernet operates only in full-duplex mode, which means there is no need for contention; CSMA/CD is not used in 10 Gigabit Ethernet
Four implementations are most common:
Implementation

## Slide 46
Implementation