## Slide 1
Other Wired Networks
Access Networks
  Networks that connect a small LAN to an ISP
Wide Area Networks
  Wired networks used to transfer data over long distances

## Slide 2
Telephone Network
The telephone network had its beginnings in the late 1800s
Plain Old Telephone System (POTS) was originally an analog system using analog signals to transmit voice
With the advent of the computer era, the network, in the 1980s, began to carry data in addition to voice

## Slide 3
Telephone Network
During the last decade, the telephone network has undergone many technical changes and the network is now Digital as well as Analog

## Slide 4
Major Components
The telephone network is made of three major components:
  Local Loops
  Trunks
  Switching offices
The telephone network has several levels of switching offices:
  End offices
  Tandem offices
  Regional offices

## Slide 5
A Telephone System

## Slide 6
A LATA can be a small or large metropolitan area
A small state may have a single LATA; a large state may have several LATAs
A LATA boundary may overlap with state boundary; part of a LATA can be in one state, part in another state
Local-Access Transport Areas (LATAs)

## Slide 7
Services offered by Telephone companies inside a LATA are called Intra-LATA services and between LATAs are called Inter-LATA services
Carrier that handles Intra-LATA are called a Local Exchange Carrier (LEC) and the ones that handle Inter-LATA are called Interexchange Carriers (IXCs)
Intra-LATA and Inter-LATA Services

## Slide 8
Switching Offices in a LATA

## Slide 9
Points of Presence (POPs)

## Slide 10
The telephone network in the beginning, used a circuit-switched network with dedicated links to transfer voice communication
The operator connected the two parties by using a wire with two plugs inserted into the corresponding two jacks
Later, the signaling system became automatic
Signaling

## Slide 11
Rotary telephones were invented that sent a digital signal defining each digit in a multi-digit telephone number
As telephone networks evolved into a complex network, the functionality of the signaling system increased
Signaling

## Slide 12
Data Transfer and Signaling Network

## Slide 13
Layers in SS7

## Slide 14
Telephone companies provide two types of services:
  Analog Services
    Analog Switched Services
    Analog Leased Services
  Digital Services
    Switched /56 Service
    Digital Data Service
Services

## Slide 15
After traditional dial-up modems reached their peak data rate, telephone companies developed another technology, DSL, to provide higher-speed access to the Internet
DSL supports high-speed digital communication over the existing telephone
Digital Subscriber Line (DSL)

## Slide 16
DSL technology is a set of technologies, each differing in the first letter (ADSL, VDSL, HDSL, and SDSL)
Digital Subscriber Line (DSL)

## Slide 17
ADSL Point-to-Point Network

## Slide 18
The Cable TV networks were initially created to provide remote subscribers access to TV programs
Cable networks enabled access to remote broadcasting stations via microwave connections
Cable TV also found a good ISP market by using some of the channels originally designed for video
Cable Network

## Slide 19
Cable TV started to distribute broadcast video signals to locations with poor or no reception in the late 1940s
It was called community antenna television (CATV) because an antenna at the top of a tall hill or building received the signals from the TV stations
Traditional Cable Networks

## Slide 20
Traditional Cable TV Network

## Slide 21
Second generation of cable network is called a Hybrid Fiber-Coaxial (HFC) network
The network uses a combination of fiber-optic and coaxial cable
Hybrid Fiber Coaxial (HFC) Network

## Slide 22
Hybrid Fiber-Coaxial (HFC) Network

## Slide 23
Cable companies are now competing with telephone companies for the residential customer who wants high-speed data transfer
DSL technology provides high-data-rate connections for residential subscribers over the local loop BUT UTP is susceptible to Interfence
Cable TV for Data Transfer

## Slide 24
This imposes an upper limit on the data rate. A solution is the use of the cable TV network
Cable TV for Data Transfer

## Slide 25
Division of Coaxial Cable Band by CATV

## Slide 26
Cable Modem Transmission System (CMTS)