## Slide 1
Connecting Devices
Hosts and networks do not normally operate in isolation
Connecting devices connect hosts together to make a network or connect networks together to make an internet
Connecting devices can operate in different layers of the Internet model

## Slide 2
Connecting Devices
Three kinds of connecting devices:
  Hubs
  Link-layer switches
  Routers

## Slide 3
Three Categories of Connecting Devices

## Slide 4
Hubs
Hub is a device that operates only in the physical layer
Signals that carry information within a network can travel a fixed distance before attenuation impacts the data
A hub (repeater) receives a signal and, before it becomes too weak or corrupted, regenerates it

## Slide 5
Hub

## Slide 6
Link-Layer Switches
A link-layer switch (or switch) operates in both the physical and the data-link layers
As a physical-layer device, it regenerates the signal it receives
As a link-layer device, the link-layer switch can check the MAC addresses (source and destination) contained in the frame

## Slide 7
Switch versus Hub
Switch has the ‘Filtering’ capability
Unlike hub, a switch can check the destination address of a frame and decide on outgoing port
Switch eliminates collisions and does not require carrier sensing
Switches connect heterogeneous devices

## Slide 8
Link-Layer Switch

## Slide 9
Learning Switch

## Slide 10
Loop Problem in a Switch
Redundant switches create Loops in the system
Created when two or more broadcasting LANs are connected by more than one switch

## Slide 11
Loop Problem in a Learning Switch (Part a)

## Slide 12
Loop Problem in a Learning Switch (Part b)

## Slide 13
Loop Problem in a Learning Switch (Part c)

## Slide 14
Loop Problem in a Learning Switch (part d)

## Slide 15
Spanning Tree Algorithm
In graph theory, Spanning Tree is a graph in which there is no loop
In a switched LAN, this means creating a topology in which each LAN can be reached from any other LAN through one path only (no loop)
To find the spanning tree, we assign a cost (metric) to each LAN link

## Slide 16
A system of Connected LANs and its Graph (Part a)

## Slide 17
A System of Connected LANs and its Graph (Part b)

## Slide 18
Finding Shortest Path/Spanning Tree for a Switch

## Slide 19
Forwarding & Blocking Ports after using Spanning Tree

## Slide 20
We compare routers to two-layer switch and a hub
A router is a three-layer device; it operates in the physical, data-link, and network layers
Routers

## Slide 21
Router vs. Switch
Three differences between a router and a repeater or a switch:
A router has a physical and logical (IP) address for each of its interfaces.
A router acts only on those packets in which the link-layer destination address matches the address of the interface at which the packet arrives.
A router changes the link-layer address of the packet (both source and destination) when it forwards the packet.

## Slide 22
A VLAN is a LAN configured by software, not by physical wiring
A station is considered part of a LAN if it physically belongs to that LAN i.e. The criterion of membership is geographic
Provides a virtual connection between two stations belonging to two different physical LANs
VIRTUAL LANS (VLAN)

## Slide 23
A Switch Connecting three LANs

## Slide 24
A Switch using VLAN Software

## Slide 25
Two Switches in a Backbone using VLAN Software

## Slide 26
What characteristic can be used to group stations in a VLAN?
Vendors use different characteristics such as interface numbers, port numbers, MAC addresses, IP addresses, IP multicast addresses, or a combination of two or more of these
Membership of a VLAN

## Slide 27
How are the stations grouped into different VLANs?
Stations are configured in one of three ways:
  Manually
  Semi-Automatically
  Automatically
Configuration of a VLAN

## Slide 28
In a multi-switched backbone, each switch must know:
  Which station belongs to which VLAN; and
  The membership of stations connected to other switches
Communication between Switches

## Slide 29
Communication between Switches
Switch A must know the membership status of stations connected to switch B, and switch B must know the same about switch A. Three methods have been devised for this purpose: table maintenance, frame tagging, and time-division multiplexing.

## Slide 30
Cost and Time Reduction
Creating virtual Workgroups
Security
Advantages of using VLANs

## Slide 31
Telco
HFC
FTTx
Comparison of Modern Access Technologies

## Slide 32
Comparison of Modern Access Technologies

## Slide 33
Fiber – The Medium of the Future!

## Slide 34
An access network in which fiber is used for part, but not the entire link from the provider to the end-user
An optical to electrical (O/E) conversion takes place somewhere near the end-user
The terminal network segment of a FTTC network is usually twisted pair or coaxial cable
Fiber To The Curb (FTTC)

## Slide 35
The final optical receiver in a FTTC network typically serves several customers
Fiber To The Curb (FTTC)

## Slide 36
Fiber To The Curb (FTTC)

## Slide 37
Need: High-speed data, reliable voice and high-quality video
Problems:
  How to get high speed lines out to each customer?
  How to future-proof the architecture?
Solution: FTTH
Fiber To The Home (FTTH)

## Slide 38
Fiber-to-the-home (FTTH) is the installation of optical fiber from a telephone switch directly into the subscriber’s home
It is one of the latest access technologies
FTTH is also referred to as Fiber-to-the-Building (FTTB)
Fiber To The Home (FTTH)

## Slide 39
Fiber To The Home (FTTH)